## Slide 1
ALLOTROPE
Vietnam's Direct Power Purchase Agreement
A practical guide for factory & industrial buyers
May 2026

## Slide 2
01
What Is DPPA?
Confidential -- For Internal Use by Allotrope & Key Partners -- Not for Further Circulation

## Slide 3
Direct Power Purchase Agreement -- Overview
Enabled by Decree 57 - Vietnam Wholesale Electricity Market (VWEM)
A DPPA is a bilateral contract that lets large electricity consumers buy renewable energy directly from generators -- bypassing the standard EVN retail tariff arrangement.
Why it matters for factories:
- Lock in a long-term renewable electricity price (the Strike Price) for 15-20 years
- Hedge against rising EVN retail tariffs
- Meet corporate RE / ESG commitments (RE100, Science Based Targets)
- Attract sustainability-focused export customers and investors
Two models exist:
- Model 1: Physical DPPA -- direct private wire from generator to factory
- Model 2: Financial DPPA -- generator sells to VWEM grid; factory buys from grid; a Contract for Difference (CfD) bridges the price
Confidential -- For Internal Use by Allotrope & Key Partners -- Not for Further Circulation

## Slide 4
Two DPPA Models
Most factories will use the Financial DPPA (Model 2) -- connected via the national grid
Model 1 -- Physical DPPA
Private wire from RE generator directly to factory site.
Suitable for:
- Factory located near a solar / wind project
- Simpler settlement (no VWEM)
- No capacity limit on generator size
- All RE technologies permitted
Limitation:
- Requires physical proximity; uncommon for distributed factory clusters
Model 2 -- Financial DPPA (CfD)
Generator sells power into VWEM. Factory buys from EVN PC at market-linked price. A financial CfD fixes the effective price.
Suitable for:
- Any large factory at 22 kV+ connection
- 200,000+ kWh average monthly consumption
- Wind, solar, or biomass plant 10 MW+
- Works across distances -- no private wire needed
Key charges:
- DPPA system charge (2025): 523.34 VND/kWh
- EVN market-linked energy + loss coefficient
- Retail tariff for unmatched shortfall hours
Confidential -- For Internal Use by Allotrope & Key Partners -- Not for Further Circulation

## Slide 5
02
Are You Eligible?
Confidential -- For Internal Use by Allotrope & Key Partners -- Not for Further Circulation

## Slide 6
Eligibility Requirements -- Financial DPPA via National Grid
Source: Decree 57 - Ecoplexus CEBA Workshop (Sep 2025)
Requirement | Detail | Factory Check
Monthly consumption | 200,000+ kWh average over prior 12 months | Approx. ~300 kW average load
Grid connection voltage | 22 kV or higher | Most medium-large industrial connections qualify
Use of electricity | Production / manufacturing purposes | Factory, industrial park, EV charging all eligible
Generator requirement | Wind, solar, or biomass 10 MW+, connected to national grid, VWEM participant | Verify generator has VWEM registration
Infrastructure | DPPA meter / metering system required | EVN PC confirms compatibility at registration
Aggregation | Currently: one buyer per CfD; aggregation proposed but not yet approved | Factory clusters should monitor regulatory updates
Confidential -- For Internal Use by Allotrope & Key Partners -- Not for Further Circulation

## Slide 7
03
How Does the Payment Actually Work?
Confidential -- For Internal Use by Allotrope & Key Partners -- Not for Further Circulation

## Slide 8
The Factory Payment Stack -- Financial DPPA
Two invoices per settlement interval: one to EVN PC, one to the RE generator under the CfD
You pay TWO parties in each trading interval:
(1) Payment to EVN PC (grid operator)
For matched DPPA volume (kWh covered by solar/wind):
Qty x FMP x Kpp + Qty x DPPA charge
For shortfall (your load > renewable output):
Shortfall kWh x EVN retail tariff
Key terms:
- FMP = SMP + CAN (wholesale market price)
- Kpp = loss coefficient (~1.027)
- DPPA charge = 523.34 VND/kWh (2025)
(2) CfD Settlement with RE Generator
Contract for Difference (CfD) formula:
Qty x (Strike Price - FMP)
- Strike Price > FMP: factory pays generator
- Strike Price < FMP: generator pays factory
The magic cancellation:
The FMP in your EVN bill and the FMP in the CfD mostly cancel. What remains is effectively:
Net matched kWh = Strike + DPPA charge
= 2,100 + 523 = 2,623 VND/kWh
Confidential -- For Internal Use by Allotrope & Key Partners -- Not for Further Circulation

## Slide 9
2025 Worked Example -- 5,000 kWh/Hour Factory Load
Assumptions from reviewed Ecoplexus / CEBA Workshop materials (2025 example inputs)
Parameter | Value | Role
Factory load | 5,000 kWh/hour | Your consumption
Strike price | 2,100 VND/kWh | Your agreed renewable price (CfD)
FMP / CFMP (wholesale) | 1,700 VND/kWh | Market reference price used in settlement
DPPA system charge (2025) | 523.34 VND/kWh | CDPPAdv (360.14) + CCL (163.2)
Loss coefficient (Kpp) | 1.027263 | Applies to FMP portion of EVN bill
Retail tariff (shortfall) | 1,833 VND/kWh | EVN retail for unmatched hours (22 kV tier)
2,670 VND/kWh
All-in matched DPPA kWh
(exact formula result)
2,623 VND/kWh
Fast shortcut estimate
(Strike + DPPA charge)
1,833 VND/kWh
Cost for unmatched kWh
(retail tariff applies)
Confidential -- For Internal Use by Allotrope & Key Partners -- Not for Further Circulation

## Slide 10
Three Settlement Scenarios Every Factory Must Understand
Solar output varies hour by hour -- your effective kWh cost shifts with it
Case A
Load > Solar Output
Factory: 5,000 kWh
Solar: 2,000 kWh matched
Shortfall: 3,000 kWh (retail)
EVN cost: 4,539,374 VND
Retail shortfall: 4,999,000 VND
CfD payment: 800,000 VND
Total: 10,338,374 VND
Blended cost: ~2,068 VND/kWh
Matched cost: ~2,670 VND/kWh
Normal -- partial RE coverage
Case B
Load = Solar Output
Factory: 5,000 kWh
Solar: 5,000 kWh matched
Shortfall: 0 kWh
EVN cost: 11,348,435 VND
CfD payment: 2,000,000 VND
Total: 13,348,435 VND
All-in cost: ~2,670 VND/kWh
(near Strike + DPPA charge)
Best case -- full RE coverage
Case C
Solar > Load (Overgen)
Factory: 5,000 kWh
Solar: 7,500 kWh generated
Excess: 2,500 kWh
CfD settled on FULL 7,500 kWh
EVN cost: 11,348,435 VND
CfD payment: 3,000,000 VND
Total: 14,348,435 VND
Effective cost: ~2,870 VND/kWh
Risk -- pay CfD on excess gen
Confidential -- For Internal Use by Allotrope & Key Partners -- Not for Further Circulation

## Slide 11
04
Key Risks & Questions to Ask Before Signing
Confidential -- For Internal Use by Allotrope & Key Partners -- Not for Further Circulation

## Slide 12
Commercial Risks & Negotiation Checklist
Five questions every factory should resolve before signing a DPPA / CfD
# | Question | Why It Matters | What to Negotiate
1 | What is the CfD settlement quantity? | Settled on generated vs. consumed vs. allocated volume -- big difference in overgen scenarios | Settle on min(generation, consumption) to cap overgen risk
2 | Are you paying CfD on excess generation? | If solar output > your load, you may pay CfD on more kWh than you consumed -- pushing cost to 2,870+ VND/kWh | Negotiate cap on contract quantity matched to your load profile
3 | What is included in the DPPA charge? | CDPPAdv and CCL may be invoiced separately; Ecoplexus proposes removing CCL | Ask for line-item breakdown; push for fee-cap clause on annual variation
4 | What loss coefficient applies to your site? | Kpp varies by connection voltage; affects exact all-in cost per kWh | Confirm Kpp in writing with EVN PC; model sensitivity
5 | What retail tariff covers your shortfall hours? | Your net saving vs. BAU depends on the time-of-use tariff you avoid -- night shortfall is cheaper than peak | Model hourly savings using your actual load profile against EVN tariff schedule
Confidential -- For Internal Use by Allotrope & Key Partners -- Not for Further Circulation

## Slide 13
05
How to Get Started
Confidential -- For Internal Use by Allotrope & Key Partners -- Not for Further Circulation

## Slide 14
Registration Process -- Financial DPPA via NSMO
National System and Market Operator (NSMO) manages the approval workflow
1
Agree in Principle with Generator
Negotiate and sign a Heads of Terms / MOU with your chosen renewable generator. Agree on Strike Price, contract term, and volume allocation (%).
2
Submit Application to NSMO
Factory submits a letter of intent + principle agreement + buyer & seller information to NSMO. NSMO reviews compliance within 5 days.
3
NSMO Notifies EVN / EVN PC
NSMO sends confirmation docs to EVN PC. EVN PC confirms metering compatibility and customer profile within 5 days.
4
NSMO Issues Expected Timeline
NSMO responds to factory with expected contract signing date between EVN and the RE generator, and the DPPA go-live date.
5
Sign CfD Contract & Go Live
CfD contract finalized between factory and generator. DPPA mechanism activated -- settlement begins on the agreed date.
Confidential -- For Internal Use by Allotrope & Key Partners -- Not for Further Circulation

## Slide 15
ALLOTROPE
Key Takeaways for Factories
(1) Your effective DPPA kWh cost = Strike Price + 523 VND/kWh (the 2025 regulated adder) -- not just the strike price
(2) The FMP cancellation effect is real: EVN market charge and CfD market reference mostly offset, leaving you close to a fixed renewable rate
(3) Over-generation is your biggest financial risk: if solar output exceeds your load, you pay CfD on more kWh than you consumed
(4) Shape your contract volume to your load profile -- avoid contracting far above your hourly consumption
(5) Minimum bar: 200,000+ kWh/month average and 22 kV connection -- check with EVN PC before engaging a generator
Live CFO calculator: https://dppa-case.web.app